EXAMPLE

Assignment # 3

This product is a garbage can.  This particular garbage can is designed to hold small pieces of garbage, yet is quite sturdy.  It weighs XXX ounces.  Garbage cans can come in many different shapes, sizes and colors.  They are generally colored to prevent having to look at the garbage in the can. This model is designed to remain indoors and is not a disposable item. It is not decorated in any way. It is probably made of Polypropylene and it should last 3-5 years.

The garbage can was created from plastic in order for it to be lightweight and durable. It does not flex in any way unless it is overloaded and the garbage is pressed down, because it is not a cyclic load, it will not need to require fatigue resistance. The can needs to be able to hold at least 25 lbs of garbage and not become distorted or fail when picked up. Because it is designed for indoor use, ultraviolet light resistance is not required. The material does need to be easily colorable for this application and it also needs to withstand common household chemicals and cleaning supplies. Due to the commercial use of this product, the material needs to be relatively cheap. There are no barrier property requirements for this product because it does not need to keep moisture, Carbon Dioxide or Oxygen from getting to the garbage. The product does need to be waterproof to prevent leaks in the event that someone throws a liquid into it. Clarity is not required for this product and neither is scratch resistance. The product should have dimensional stability to prevent it from being deformed when full of garbage. The garbage can should be able to withstand temperatures within the range of 40-90 degrees F.